## Slide 1: Hands on Workshop

## Slide 2: Introduction to Robotics 1 3 4 2
Role of Engineers in robotics
Contemporary Robots
Basic Component of Robots
Types of Robots

## Slide 3: Components of Robots
Sensors (Eyes, Ears, Nose)
Controller (Brain)
Actuators (Legs, Hands)

## Slide 4: Microcontroller
It is designed to perform specific Applications
It has got fixed amount of RAM, ROM and other peripheral components on a single chip
Applications: Keyboards, Mouse, Washing machine, Digicam etc

## Slide 5: Arduino 1

## Slide 6: Arduino Boards
Arduino Nano
Arduino Mini
Arduino Mega

## Slide 7: Arduino UNO

## Slide 8: Arduino Components
Microcontroller ATmega328
Operating Voltage 5V
Input Voltage (recommended)7-12V
Digital I/O Pins 14
(of which 6 provide PWM output)
Analog Input Pins 6
DC Current per I/O Pin 40 mA
DC Current for 3.3V Pin 50 mA

## Slide 9: Power Supply

## Slide 10: Arduino Software
http://arduino.cc/en/Main/Software
Download Software
unzip the folder.
launch the programming environment.
install a driver that comes with Arduino - communication

## Slide 11
Actual Code
(Editor)
Message Box
Compile
(verify)
Upload

## Slide 12: Configuring IED
Actual Code
(Editor)

## Slide 13
Board Name
&
Port No.

## Slide 14: Serial Monitor
Actual Code
(Editor)
Serial Monitor

## Slide 15: PWM (Pulse Width Modulation) Control
Used to control motor speed
6 PWM pins (3,5,6,9,10,11), can also be used as Digital IO
Values vary from 0-255
For speed control:
5V Potential - Analog Value 225/ Digital Value 1 = Full Speed of 150RPM
0V Potential - Analog Value 0 / Digital Value 0 = Zero Speed
Analog Value = Duty cycle * 255
Where,
% duty cycle = % speed

## Slide 16: Instructions
pinMode( pin number, state );
state- INPUT/OUTPUT pin number- pin you are using
digitalWrite( pin number , state ); state- HIGH/LOW
digitalRead( pin number);
analogRead( pin number);
pin number- 3,5,6,9,10,11 analog value- 0 to 255 (depends on speed)

## Slide 17: Conditions & Loop
While (condition) {………}
If ( condition ) {……..} else if (condition) {……..} else (condition) {……….}

## Slide 18: Arduino Programing
Two mandatory functions:
1. void setup()
{
// the setup routine runs once when you press reset or when you powered it ON.
}
2. void loop()
{
// the loop routine runs continuously
}

## Slide 19: PROGRAM TO GLOW AN LED
void setup()
{
pinMode(13,OUTPUT);
}
void loop()
{
digitalWrite(13,HIGH);
}
pinMode:
Syntax:
pinMode(<pin no.>,<mode>);
pin no. : 0 – 13
mode : OUTPUT / INPUT
digitalWrite:
Syntax:
digitalWrite(<pin no.>,<State>);
pin no. : 0 -13
State : HIGH / LOW or ON/OFF

## Slide 20: PROGRAM TO BLINK AN LED
int led = 13;
// the setup routine runs once when you press reset
void setup() {
// initialize the digital pin as an output.
pinMode(led, OUTPUT);
}
// the loop routine runs over and over again forever:
void loop() {
digitalWrite(led, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(led, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}

## Slide 21: Building the Robot 2

## Slide 22
ASSEMBLING

## Slide 23: Components Provided
SI No | Components
1 | Robot chasis
2 | Castor Wheel
3 | H-Bridge
4 | 150 rpm motors
5 | F-F wires
6 | M-F burg wires
7 | Bluetooth module
8 | IR sensor
9 | Micro switch
10 | Lead acid battery
11 | Wheels
12 | L293D IC
13 | Battery chips
14 | Arduino board
15 | Screw & nuts
16 | Screw driver

## Slide 24: Step 1 – Attach Motors to chasis

## Slide 25: Step 2 – Attach Wheels

## Slide 26: Step 3 – Fix castor wheel

## Slide 27: Step 4 – Attach Battery, H bridge, Arduino

## Slide 28: Do’s & Don’t
Don’t connect the battery directly to the Arduino board.
Pay attention in handling the batteries
Don’t Reverse the terminal
Red – (+)ve; Black – (-)ve.

## Slide 29: Motors
Motor – Types
Motor driver
Differential drive

## Slide 30: Motors
Stepper Motor
Servo Motor
Brushless DC
DC Motor

## Slide 31: Differential Drive 3

## Slide 32
Moving Straight
To Spin

## Slide 33
Moving Straight
To Spin
33
Longer Turn
Shorter Turn

## Slide 34: H-Bridge

## Slide 36: Program to Drive a Motor
// declarations of pins
int r_in1_a = 2,r_in1_b = 3;
void setup() {
// initialize the digital pin as an output.
pinMode(r_in1_a, OUTPUT);
pinMode(r_in1_b, OUTPUT);
}
void loop()
{
digitalWrite(r_in1_a, HIGH);
digitalWrite(r_in1_b, LOW);
}

## Slide 37
// declarations of pins
int r_in1 = 2,r_in2 = 3;
int l_in1 = 4,l_in2 = 5;
void setup() {
// initialize the digital pin as an output.
pinMode(r_in1, OUTPUT);
pinMode(r_in2, OUTPUT);
pinMode(l_in1, OUTPUT);
pinMode(l_in2, OUTPUT);
}
void loop()
{
digitalWrite(r_in1, HIGH);
digitalWrite(r_in2, LOW);
digitalWrite(l_in1, HIGH);
digitalWrite(l_in2, LOW);
}

## Slide 38: Try These
Both motors – Forward.
Both motors – Backward.
Turn Left
Turn Right
Spin the robot

## Slide 39: Speed Control
PWM – Speed control
6 PWM Pins (3,5,6,9,10,11)
Values vary from 0-255
For speed control:
5V Potential - Analog Value 225/ Digital Value 1 = Full Speed of 150 RPM
0V Potential - Analog Value 0 / Digital Value 0 = Zero Speed

## Slide 40: Program to control the speed
pinMode(<PWM pin>, OUTPUT);
void loop()
{
analogWrite(<pin no.>,<value>);
}
// declarations of pins
int r_in1 = 3,r_in2 = 5;
void setup() {
// initialize the digital pin as an output.
pinMode(r_in1, OUTPUT);
pinMode(r_in2, OUTPUT);
}
void loop()
{
analogWrite(r_in1, <0-255>);
analogWrite(r_in2, <0-255>);
}

## Slide 41: Sensing the environment 4

## Slide 42: Line Follower
Sense the presence of line
Sensor – IR sensor

## Slide 43: IR Waves
IR –Infrared waves
They are part of the Electromagnetic Radiation
Range:700nm to 1mm
Applications: Remote sensors, CCTV cameras, Thermal Imaging and Astronomy

## Slide 44
White – Transmitter
Black – Receiver
Dark colored object absorbs
the light (Less Reflection)
Light Colored objects reflects the
Light (More Reflection)
Surface | Sensor Output
Black | 5v(HIGH)
White | 0v(LOW)

## Slide 45: Line Follower Logic
If Sensor detects Black Line
Move left for 500ms
Move Right
True
False

## Slide 46
// declarations of pins
int sen1=4,sen2=5;
int state1,state2;
void setup()
{
// initialize the digital pins as an input.
pinMode(sen1, INPUT);
pinMode(sen2, INPUT);
}
void loop()
{
state1 = digitalRead(sen1);
state2 = digitalRead(sen2)
}
Sen1 (Left) | Sen2 (Right) | Action
Low | Low | Go Straight
Low | High | Turn Right
High | Low | Turn Left

## Slide 47: Edge Detection
Sense the absence of path
Sensor – IR sensor

## Slide 48: Line Follower Logic
If Sensor detects empty space
Move left for 500ms
Move Right
True
False

## Slide 49
// declarations of pins
int sen1=4,sen2=5;
int state1,state2;
void setup()
{
// initialize the digital pins as an input.
pinMode(sen1, INPUT);
pinMode(sen2, INPUT);
}
void loop()
{
state1 = digitalRead(sen1);
state2 = digitalRead(sen2)
}
Sen1 (Left) | Sen2 (Right) | Action
High | High | Go Straight
Low | High | Turn Right
High | Low | Turn Left
Low | Low | Turn Left

## Slide 50: Any Questions

## Slide 51: Thanks You!